## Slide 1: Grey Water - 2

## Slide 2: Presentation Scope
In this presentation you will learn:
  Greywater composition
  Greywater treatment

## Slide 3: Water classification

## Slide 4: Grey Water
Grey water sources :

## Slide 5: Grey water composition
Grey water sources | % Generated | contaminants
Grey water from bathroom | 50% -60% | soap, shampoo, hair dye, toothpaste, cleaning products
Grey water from cloth washing | 25% -35% | faecal contamination with the associated pathogens and parasites such as bacteria
Grey water from kitchen | 8% - 10% | Contaminated with oil, food particles and other wastes which supports growth of micro-organisms . It also contains chemical pollutants such as detergents and cleaning agents which contains various chemicals

## Slide 6: Possible Uses Of Treated Grey Water

## Slide 7: Basic Grey Water Treatment
Screening
Filtered water
Primary treatment stage
Grey water
Secondary treatment stage
Final treatment stage

## Slide 8: Basic Grey Water Treatment
Liquid Waste (Sewage/Wastewater) Treatment Wastewater (liquid waste) from flushing the toilet, bathing, washing sinks and general cleaning goes down the drain and into a pipe, which joins a larger sewer pipe under the road.
STAGE ONE: SCREENING Screening is first stage of the wastewater treatment process. Screening removes large objects like, sanitary items, cotton buds, face wipes and even broken bottles, bottle tops, plastics and rags that may block or damage equipment. Special equipment is also used to remove grit that gets washed into the sewer.

## Slide 9: Basic Grey Water Treatment
STAGE TWO: PRIMARY TREATMENT This involve the separation of organic solid matter from the wastewater. This is done by putting the wastewater into large settlement tanks for the solids to sink to the bottom of the tank. The settled solids are called ‘sludge’. At the bottom of these circular tanks, large scrappers continuously scrape the floor of the tank and push the sludge towards the center where it is pumped away for further treatment. The rest of the water is then moved to the Secondary treatment.

## Slide 10: Basic Grey Water Treatment
STAGE THREE: SECONDARY TREATMENT The water, at this stage is put into large rectangular tanks. These are called aeration lanes. Air is pumped into the water to encourage bacteria to breakdown the tiny bits of sludge that escaped the sludge scrapping process.

## Slide 11: Basic Grey Water Treatment
STAGE FOUR: FINAL TREATMENT Next the ‘almost’ treated wastewater is passed through a settlement tank. Here, more sludge is formed at the bottom of the tank from the settling of the bacterial action. Again, the sludge is scrapped and collected for treatment. The water at this stage is almost free from harmless substances and chemicals. The water is allowed to flow over a wall where it is filtered through a bed of sand to remove any additional particles. Note :This description is not a standard for all treatment plants, but the principle is similar.